## Slide 1: Rotor Drive Tuning
Matt Fowler
6/23/2020

## Slide 2: Initial Tuning
Initial tuning was performed without blades attached
Results in R32_I64_20210429_1244.ccx

## Slide 3: Re-tuned
Auto Tune was performed with blades attached
Motor Position Wrap changed from “0” to “4096”
Saved as “R32_I64_20210623_1647.ccx”

## Slide 4: Motor Data
Rated Speed from datasheet
  Kennlinie_cyber_d_32__5012-D027865-03 (2).pdf
Other values from previous tuning

## Slide 5: Current Loop Auto Tune

## Slide 6: Auto Phase
Jog > yielded CW rotation looking downwind (positive rotation)

## Slide 7: Velocity Loop Auto Tune

## Slide 8: Manually detuned Velocity Loop
Try to reduce any amplification due to load from controller
Vp = 25, Vi=50

## Slide 9: Retune, 9/14/2021
Cp = 286
Ci = 47

## Slide 10: Labview Ctrl Tuning, 9/20/2021
Cp = 525
Ci = 3